## Slide 1: BATTLEZONE
F15-18545 (Team MX-Butterfly)
Ashish Shrestha
Hui Jun Tay
Peter Pearson

## Slide 2: PRESENTATION OVERVIEW
Battlezone (What, Why, Where)
System Architecture Overview
  6502 Core
  Memory Infrastructure
  Analog Vector Generator
  MathBox
  POKEY
What we’ve learned
  Things to watch out for
Conclusion

## Slide 3: BATTLEZONE
Originally called “Moon Tank”
Drive a tank, shoot at other tanks
  Two joysticks with buttons
Vector graphics
3-D game world

## Slide 4: FINAL STATUS
Working copy of the game
  Some sounds missing
Make option switches accessible
Cabinet

## Slide 5: SYSTEM ARCHITECTURE OVERVIEW
6502 CORE
AVG
POKEY
AUDIO
CONTROLS
VGA
RASTERIZER
LINE REGISTER QUEUE
FRAME BUFFER
PROGRAM RAM
ADDRESS DECODER
PROGRAM ROM
MATHBOX
VECTOR
RAM/ROM
NMI

## Slide 6: 6502 PROCESSOR
Using OpenCores 6502 processor
  Fixed a small bug involving decimal mode
Handles game flow and most calculations
6502 CORE

## Slide 7: 6502 processor - interfacing
Graphics
  Writes into graphics memory
MathBox
  Writes calculation requests, reads results
POKEY
  Sound, controls, RNG
NMI Counter
6502 CORE
AVG
POKEY
ADDRESS DECODER
MATHBOX
VECTOR
RAM/ROM
NMI

## Slide 8: MEMORY INFRASTRUCTURE
Address Decoder
  Program RAM
  Program ROM
  Vector RAM/ROM
  Memory Mapped I/O (Pokey/MathBox)
  Settings and miscellaneous signals
6502 CORE
PROGRAM RAM
ADDRESS DECODER
PROGRAM ROM
MATHBOX
VECTOR
RAM/ROM
POKEY

## Slide 9: ANALOG VECTOR GENERATOR (AVG)
Reads instructions from Vector RAM/ROM
Communication with 6502 processor
Draws lines for game
9 Instruction ISA
Runs at 6 MHz
6502 CORE
AVG
ADDRESS DECODER
VECTOR
RAM/ROM

## Slide 10: AVG - INTERFACING
Connects to line register hardware queue
Queues up endpoints of lines for rasterizer
Reads instructions from memory
Uses two ports of different sizes to get 8/16-bit instructions
AVG
LINE REGISTER QUEUE
VECTOR
RAM/ROM
16-bit
8-bit

## Slide 11: AVG - RASTERIZER
Bresseham’s line algorithm
One pixel of output per clock cycle
Uses linear geometry to calculate dependent offsets of line coordinates
RASTERIZER
LINE REGISTER QUEUE
FRAME BUFFER

## Slide 12: AVG - FRAME BUFFER
640x480 VGA output
Switch between two BRAMs
Rasterizer draws (writes) to one, VGA reads from other
4-Bit intensity value
Addressed by row/col counter
VGA
RASTERIZER
A
B
LINE REGISTER QUEUE
FRAME BUFFER

## Slide 13: MATHBOX
Math co-processor
  Used for 3-D calculations (rotations, translations)
  Primarily does fixed-point multiplication/division
  Treated as memory mapped I/O
6502 CORE
ADDRESS DECODER
MATHBOX

## Slide 14: MATHBOX
Proprietary, nearly no documentation
  MAME has software implementation
    Abstracted own implementation based on source
  Abusing faster hardware for design
6502 CORE
ADDRESS DECODER
MATHBOX

## Slide 15: POKEY I/O - CONTROLS
Analog-digital converters to read controls
Core polls POKEY for controls
6 (functional) buttons attached by GPIO pins
  Two forward/backward (one for each joystick)
  Two firing buttons (functionally one)
  Start button
6502 CORE
POKEY
CONTROLS
ADDRESS DECODER

## Slide 16: POKEY I/O - RNG
Hardware RNG
Linear feedback shift register
Used in sound and in-game
6502 CORE
POKEY
ADDRESS DECODER
RNG

## Slide 17: POKEY I/O - Sound
Four audio channels
  Core writes to determine frequency/volume (per channel)
  Uses frequency divider to get final sound
6502 CORE
POKEY
AUDIO
ADDRESS DECODER

## Slide 18: POKEY I/O - Sound
Some sound is external to POKEY
Capacitive discharge
  Used to create fading sounds
  Bullets, explosions, engine
Triggered by 6502 writes
6502 CORE
POKEY
AUDIO
ADDRESS DECODER
BREAKOUT BOARD

## Slide 19: FINAL HARDWARE SETUP
Nexys4 board running game
Sony VGA Monitor with “arcade overlay”
POKEY
  Dual external speakers
  Push-button joysticks + arcade buttons
Wood arcade cabinet mount
    Coin-door stretch goal

## Slide 20: LESSONS LEARNED
Watch out for proprietary hardware
MAME is a godsend
Overshoot on expected FPGA specs
Vivado...

## Slide 21: WHAT TO WATCH OUT FOR
Don’t trust Ryan with your core
Be willing to ignore the schematics
Don’t assume that old devs cared about protocol
Vivado...

## Slide 22: CONCLUSIONS
Vector graphics surprisingly complex
Reverse engineering specifications
  Frustrating & Fun
Long hours of debugging small issues
Vivado…

## Slide 23: Tank you
Q&A