## Slide 1
Originally an analog component
  Electron gun moved around screen and drew lines
9 instruction ISA for a mini-processor
Re-designed for this project in a digital manner
  Built a 9-instruction processor
  Reads from vector RAM/ROM
  16-Bit reads from memory
Sends line information to Rasterizer
Debugged with custom-built tool chain
  Software simulator
  Assembler/Disassembler
FRAME BUFFER
6502 CORE
AVG
POKEY
AUDIO
CONTROLS
VGA
RASTERIZER
LINE REGISTER QUEUE
FRAME BUFFER
PROGRAM RAM
PROGRAM ROM
MATHBOX
VECTOR
RAM/ROM
NMI
ADDRESS DECODER
F15 18545 Digital Design Project
TEAM M-X BUTTERFLY
Ashish Shrestha
Hui Jun Tay
Peter Pearson
6502 Core
Standard 6502 Core
  15-Bit address bus
  8-Bit data bus
  Used in many old consoles/games
Open source Verilog description
  Made by Arlet Ottens
  Fixed bug in decimal mode
  Passed verification
Runs at 3 MHz
Periodic non-maskable interrupts
One-cycle read latency
Addressing and Memory
Memory System
  Used Vivado Block RAM for all memory
  Divided memory into blocks by function
Memory Mapped I/O
  POKEY and Math Box
Address decoding
  Takes addresses from 6502, sends to different memory partitions
  Reads and writes to memory mapped I/O
Math Box
Proprietary hardware piece
  Hard to find specifications
Handles rotations
  Fixed point multiplication & division
Built using MAME as reference
Analog Vector Generator
Graphics
Rasterizer
  Bresseham’s line algorithm
Line Register Queue
  Buffers output from AVG to Rasterizer
Frame Buffer
  Double-buffer (Read/Write)
  Outputs to 640x480 VGA
  Stores 4-bit intensity
  Hard-coded red/green pixels
WRITE
READ
RASTERIZER
VGA
“The math box was passed a 2x2 rotation matrix and -- I believe -- a list of points to rotate. If I remember correctly translation was handled in the 6502, although this may have been done in the math box as well. It's been a long time.”
-Ed Rotberg, Programmer for Battlezone
POKEY I/O
6 buttons attached by GPIO pins
  Joysticks correspond to tank treads
  Analog-digital converters read controls
  6502 polls POKEY for controls
Four audio channels
  6502 writes frequency/volume to POKEY
  Uses frequency divider for final sound
  Capacitive discharge (fading sounds)
Hardware RNG
  Linear feedback shift register